## Slide 1: ROS topic, Node and Messages
Session 4

## Slide 2: Node
Let’s start with something simple, turtlesim

## Slide 3
>> roscore
In a new terminal,
>> rosrun turtlesim turtlesim_node

## Slide 4
In a new terminal
>> rqt_graph
In a new terminal,
>> rosnode list – to visualize available nodes
CTRL + C
>> rostopic list – to visualize available topic
In a new terminal,
>> rosrun turtlesim turtle_teleop_key

## Slide 5
Make sure the active window is the “rosrun turtlesim turtle_teleop_key”
Use arrow keys to move the turtle.

## Slide 6
Node is like a function
Topic is the tunnel for data transmission
The relationship between Node and other node are connected with topic, and is unlimited
IMPORTANT – if there is no node, no topic can be transfer

## Slide 8
Publish and Subscribe

## Slide 9: Two Ways to Publish
1. Use command
  rostopic pub /topic_name
2. Use coding in python

## Slide 10: Task
Create new file called message_pub.py in /innokai_workshop_ws/src/ros_basic/src

## Slide 11: ROS topic, Node and Messages
Session 5

## Slide 12: Publish
Publish means sending data/value
initiate node with node name
initiate Publisher with
Topic name
publish to Topic

## Slide 13
>> chmod +x message_pub.py  Change Mode
make the file executable
In a new terminal
>> roscore (important, rosrun need to have a master node)
In a new terminal
>> rosrun ros_basic message_pub.py

## Slide 14
In a new terminal
>> rostopic echo /counter
TASK
Initiate a node called “calculator”. Publish to topic “/result”
Calculate the difference of
Group 1 = 99, 88, 77 and Group 2 = 77, 88, 99

## Slide 15: Twist Message Type
In a new Terminal
>> rosmsg show geometry_msgs/Twist

## Slide 16: Twist Message Type
Linear velocities are specified in meters per second.
Angular velocities are given in radians per second.
For Turtlebot3, linear “x” is used for forward motion.
Angular “z” used for rotation.

## Slide 17: Testing Twist in turtlesim
Use command
In a new terminal
>> rostopic pub /turtle1/cmd_vel geometry_msgs/Twt "linear:
x: 2.0
y: 0.0
z: 0.0
angular:
x: 0.0
y: 0.0
z: 0.0"
Modify these two values to have different motion

## Slide 18
Use coding

## Slide 19: Turtlebot3 Navigation
In a new terminal
>> roslaunch turtlebot3_gazebo turtlebot3_world.launch
In a new terminal
>> rostopic list
*Tips, normal all robot use similar name
cmd_vel, velocity, etc

## Slide 20: Turtlebot3 Navigation Publish
Use command
In a new terminal
>> rostopic pub /cmd_vel geometry_msgs/Twist "linear:
x: 0.0
y: 0.0
z: 0.0
angular:
x: 0.0
y: 0.0
z: 2.0"

## Slide 21
Use coding

## Slide 22: Use Time and Duration in ROS
In programming, normally we CANNOT define how far can a robot go, we can define the duration of a robot move or how many rotation
Here we learn about time and duration
Rotation will not be cover in this session

## Slide 23: Time and Duration arithmetic
1 hour + 1 hour = 2 hours (duration + duration = duration)
2 hours - 1 hour = 1 hour (duration - duration = duration)
Today + 1 day = tomorrow (time + duration = time)
Today - tomorrow = -1 day (time - time = duration)
Today + tomorrow = error (time + time is undefined)

## Slide 24: Recall
rospy.sleep(duration)
ROS will sleep for the specified period
rospy.Rate(hz)
maintaining a particular rate for a loop

## Slide 25: Timer
rospy.Timer(period, callback, oneshot=False)
Timer instance will attempt to call the callback every n seconds.

## Slide 26: Example Usage
Move turtlebot3 forward for 10 sec

## Slide 27: Task
Move your turtlebot forward for three second and stop for 2 second. In the end, spin 180°.

## Slide 29: Subscribe
All the previous slide are about publish (send data)
Subscribe is about receiving data

## Slide 30: Subscribe
In src folder of ros_basic, create topic_subscriber.py and chmod +x it

## Slide 31: Example
In two different terminal
>> rosrun ros_basic message_pub.py
>> rosrun ros_basic topic_subscriber.py

## Slide 32: Usage
Receive data from sensors
Receive data from nodes
Data source (topic name)
Data type receiving
Callback function to process the data

## Slide 33
In bracket is the data, this case
we name it “msg”
Below is the coding to process the data

## Slide 34: Task
Create two different .py file, one for publish while another one is subscribe
Topic
Send string “Hello World”
Subscribe
Print the data received
*(you may use print or rospy.loginfo)

## Slide 35: Camera and Sensor Implementation
Session 6

## Slide 36: Sensors
In ROS, many sensors are supported:
Camera, ultrasonic sensors, LDS, RGB-D camera, Touch Sensors, Gyroscope 3 Axis, Accelerometer 3 Axis, Magnetometer 3 Axis, etc.

## Slide 37: Task
Move turtlebot forward until the distance in front is 1.0m

## Slide 38: LDR Test
>> roslaunch turtlebot3_gazebo turtlebot3_stage_1.launch
In a new terminal
>> rosrun ros_basic ldr.py

## Slide 39
ldr.py

## Slide 40: LDS(Laser Distance Sensor)
Data is read in these direction
360 Laser Distance Sensor LDS-01

## Slide 41: Computer vision in ROS
Standardized package manager
Runs on Ubuntu
Standardizes message-protocols for:
  Pose estimation
  Localization
  Navigation
  Computer vision
Incorporates the latest contributions from academia
Andrew Symington, UCL Gazebo and rviz with several quadrotors, ROSCon 2014

## Slide 42: End of DAY 2
See you tomorrow